Mods:	Give paths to all subroutines called in each project intro

Bugs found in PCB111000_CP2102_projects
Arduino_Rx_Tx_UNO_pcb.c file: .
1 effects use of backspace key in Int/FloatNum_from_PC_A()
if(num_as_string[m] != '\b');
 // else for(int p = m; p < strln-1; p++){num_as_string[p-1] = num_as_string[p+1]; num_as_string[p+1] = '\0';m = 0;} }
else for(int p = m; p < strln-1; p++){num_as_string[p-1] = num_as_string[p+1]; num_as_string[p+1] = 0;num_as_string[p] = 0;m = 0;} }

2 prevents print out of Sc_Num_to_PC_A(Result,0,6,'\r');	The 0 must be at least 1
if(pre_dp){
while(--pre_dp){A = A*10;}	//Convert FPN to Scientific format (real + exponent)
while (num >= A){num = num/10.0; Exp += 1;}
while (num <= A){num = num*10.0; Exp -= 1;}}

3 In 6F_FPN_from_IO and 6H_calculator
float FPN_number_from_IO(void) updated as below
dp_control = 0;
exp_control = 0;
neg_sign = 0;
scroll_control = 0;

4	5_Arduino_PC_comms_library\5C_Scientific_numbers
This has been rewritten
See PCB111000_CP2102_projects version

5	Bug found in KBD_to_display\long Int_KBD_to_display() and float	Float_KBD_to_display()
Effects use of backspace key

Pin change interrupts:	Use pci not PCI

1_first_project
Example_1	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_2	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_3	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_4	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_5	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_6	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_7	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_8	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_9	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_10	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

2_Receiver_Transmitter_Basic
Example_1	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_2	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_3	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_4	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_5	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_6	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_7	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_8	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
Example_9	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

3_Interrupts_and_switches
3A_UART_timer_interrupts	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3B_Pin_Change_Interrupt	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3C_reaction_time_tester	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3D_timer_PCI_interrupts	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3E_Keypress_logger	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3F_Prime_numbers	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3G_Prime_numbers_plus	OK	CC_OK	CA_ARD_OK	CC_ARD_OK

4_binary_and_bit_operations
1_Bit_ops_1	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
2_Bit_ops_2	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
3_Division_subroutine	OK	CC_OK	CA_ARD_OK	CC_ARD_OK
4_Char_to_binary	OK	CC_OK	CA_ARD_OK	CC_ARD_OK

 5_Arduino_PC_comms_library and 6_The_8_digit_display_and_IO

Arduino_Rx_Tx_UNO_pcb\
Unsigned_Int_from_PC_A();
Int_Num_from_PC_A();
Sc_Num_from_PC_A();
Unsigned_Int_to_PC_A();
Int_Num_to_PC_A();
Sc_Num_to_PC_A();

KBD_to_display\
Int_KBD_to_display_A();
FPN_KBD_to_display_A();
FPN_string_KBD_to_display_A();

 FPN_DIY_IO\
I2C_FPN_to_display();

5A_Integer_numbers	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
5B_Prime_factors	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
5C_Scientific_numbers	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
5D_Pie_estimator	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
5E_e_power_series	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
5F_Trig_functions	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

6A_Segment_driver	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6B_Segment_driver	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6C_Numerical_entry	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6D_INT_to_display	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6E_FPN_to_display	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6F_FPN_from_IO	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6G_INT_from_IO	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6H_calculator	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6L_FPN_to_display_legacy	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
6M_FPN_from_IO_legacy	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

7 Timer/clocks	No local functions
7A-F updated and recompiled G not changed (has no commentary)
7A_String_only_clock	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7B_calculator_based_clock	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7C_mini_OS_clock	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7D_mini_OS_clock_w_a	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7E_Stand_a_lone_clock	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7F_Stop_watch	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
7G_Combined_clock_SW	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

8_Fourier	Commentary mode not used
8A_reset_controller	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
8B_Pulse_train_generator	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
8C_Sawtooth_generator	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

9_FPN_routines
9A FPN_acquisition	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
9B_FPN_to_String	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
9C_FPN_Add_Sub	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
9D_FPN_mult_div	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK
9E_e_power_series	CA_OK	CC_OK	CA_ARD_OK	CC_ARD_OK

Proj_9 subroutines used

FPN_DIY_IO\
I2C_Tx_float_display_control;
Scientific_number_from_KBD();
Fraction_to_Binary_Signed();
Scientifc_num_to_FPN();
I2C_Tx_float_num();
I2C_FPN_to_display();
Assemble_FPN();
unpack_FPN();
FPN_to_String();

All subroutines included under “FPN_DIY_IO” used and tested in “9_FPN_routines”

KBD_to_display\
Get_fpn_from_KBD();
Get_Float_num_string_from_KBD();

Arduino_Rx_Tx_UNO_pcb\
Sc_Num_to_PC_A();
FPN_to_Significand();

FPN_arithmetic\
FPN_add();
FPN_div();
FPN_mult();

Basic_Rx_Tx_Arduino\
Check_num_for_to_big_or_small();

Print_RHS_of_binary_point();	Local only
Print_long_as_binary();	Local only

Mini OS EEPROM reservations

0x3FF	user cal if set
0x3FE	user cal if set
0x3FD	Default cal supplied by Atmel

0x3FC	Set to 1 if diagnostic mode required. Diagnostic mode is now discontinued
0x3FB	Controls multiplexer (T0) on interval: 0xFF for 2ms, 0xFE for 500uS and 0xFD for 125uS
0x3FA	Not used
0x3F9	Reset status byte: set to zero by Project_programmer_AVR when the mini-OS is programmed to flash.	It is read here to ensure that control always jumps to location zero except for a manual reset

0x3F8	prog_counter_H
0x3F7	prog_counter_L
0x3F6	cmd_counter_H
0x3F5	cmd_counter_L

0x3F4	Reset status byte: set to zero by Project_programmer_AVR. When the mini-OS is programmed to flash.	It is read by I2C_V16_0_CC to ensure that the UNO bootloader is automatically triggered after pcb_A has been programmed

0x3F3	8 bit PRN gen EEP subroutines:	Used to select random "Hello world" message
0x3F1	Carry out auto cal post programming

UNO_bootloader_for_hex&text	EEPROM reservations

1_Message_from_the_OS
2_Random_gen_AVR
3_Hex_verification
4_Text_Verification
5_Hex_text_bootloader

0x3FF	user cal if set	No longer used
0x3FE	user cal if set No longer used
0x3FD	Default cal supplied by Atmel No longer used
0x3FC	Copy of MCUSR and also indicates WDTout hex/text verification routines
0x3FB/A	prog_counter for use by verification routines
0x3F9/8	cmd_counter for use by verification routines
0x3F7	Reset Control (set to zero to indicate that user app is to be launched.)
0x3F6 flash text string pointer

0x3F5 PRN generator random number HB
0x3F4 PRN generator random number LB
0x3F3 PRN generator random number HB
0x3F2 PRN generator random number LB
0x3F1 PRN generator random number HB
0x3F0 PRN generator random number LB
0x3EF PRN EEPROM location offset 0, 1 or 2
0x3EE Used by combined Clock_SW to signal Arduino WDTout with ISR
0x3ED Used by user projects to control WDT reset source
0x3EB	Last EEPROM location required by Hello World file

EEPROM initialisation	Mini_OS (PCB_A)

0x3FD/E/F	Cal data:	Calibration routine
0x3FC	No longer used
0x3FB	Multiplexer brightness	Mode Q
0x3FA	No longer used
0x3F9	Reset status byte:	Project Programmer UNO
0x3F8-5	Command counters	Flash programmer
0x3F4	Reset status byte:	Project Programmer UNO
0x3F3	Hello world PRN
0x3F2	Not used
0x3F1	Auto call flag	Project Programmer UNO

EEPROM initialisation	UNO_bootloader_for_hex&text

0x3FD/E/F	Cal data:	No longer used
0x3FC	Copy of MCUSR	The boootloader
0x3FB-8	Command counter	Bootloader
0x3F7	Reset Control	The boootloader
0x3F6	flash text string pointer	User_app_commentary_mode
0x3F5-0	PRN registers	Not initialised	0xFF or > 0
0x3EF	PRN EEPROM offset	Zero by PCB_A programmer
0x3EE Used by combined Clock_SW to signal Arduino WDTout with ISR
0x3ED Used by user projects to control WDT reset source
0x3EB	Last EEPROM location required by Hello World file

Mini-OS modes no longer required

case 7: I2C_Tx_Compile_tables();break;
case 8: I2C_Tx_2URNs_from_IO();break;	//Generates numbers of type 0.1234 With an	exponent
case 9: I2C_Tx_Uarithmetic_OP();break;	//Takes numbers entered using mode B and does	some arithmetic

case 'A': I2C_Tx_accumulator_1();	break;	//Implements add, subtract and clear modes
case 'B': I2C_Tx_accumulator_2();break;	//Acquires data for use by accumulator